## Ketton Parish Council: Hall Close Play equipment Risk Assessment – reviewed by H&OS 25/09/2019 &Full Council May 2020

| Time Period Covered | April 2020– March 2021 | Location | Hall Close, Ketton |
| --- | --- | --- | --- |
| Activity | Public use of Children’s play area |
| People covered by risk assessment: | Children, General Public and KPC Staff. |

| The Hazard | Location of the Hazard | Who could be harmed? | Level of risk | Controls | Implementation/ Monitoring |
| --- | --- | --- | --- | --- | --- |
| Failure of chains | Swings | Children General Public KPC Staff | low | Chains to be checked for wear at touching points and replaced when reach 40% wear weekly visual check monthly operational inspection Yearly independent play inspection | Implemented by KPC handymen Monitored by Parish Clerk & H&OS Committee Quarterly inspection carried out by an RPII Inspector (Wicksteed Leisure) on 02/04/2019,29/10/2019 & 22/01/2020 |
| Slips, trips and falls caused by uneven ground | Children’s play area | Children General Public KPC Staff | med | Weekly visual check Monthly operational inspection Yearly independent play inspection | Implemented by KPC handymen Monitored by Parish Clerk & H&OS Committee Quarterly inspection carried out by an RPII Inspector (Wicksteed Leisure) on Inspector (Wicksteed Leisure) on 02/04/2019,29/10/2019 & 22/01/2020 |
| Falling from built structures | Children’s play area | Children General Public KPC Staff | low | Monthly operational inspection Grass surface and matting to be maintained, no hard objects within 150mm of grass surface Yearly independent play inspection | Implemented by KPC handymen Monitored by Parish Clerk & H&OS Committee Quarterly inspection carried out by an RPII Inspector (Wicksteed Leisure) on Inspector (Wicksteed Leisure) on 02/04/2019,29/10/2019 & 22/01/2020 |
| Failure of structures (rotting timber) | Children’s play area | Children General Public KPC Staff | low | Weekly visual check Monthly operational inspection Yearly independent play inspection | Implemented by KPC handymen Monitored by Parish Clerk & H&OS Committee Quarterly inspection carried out by an RPII Inspector (Wicksteed Leisure) on Inspector (Wicksteed Leisure) on 02/04/2019,29/10/2019 & 22/01/2020 |
| Failure of rope | Multi play unit Basket swing | Children General Public KPC Staff | med | Weekly visual check Check for wear of outer covering Monthly operational inspection Yearly independent play inspection | Implemented by KPC handymen Monitored by Parish Clerk & H&OS Committee Quarterly inspection carried out by an RPII Inspector (Wicksteed Leisure) on Inspector (Wicksteed Leisure) on 02/04/2019,29/10/2019 & 22/01/2020 |
| Finger trap | Cracking timber | Children General Public KPC Staff | low | Monitor wooden structures for natural cracking. Fill if larger than 10mm wide. Monthly operational inspection Yearly independent play inspection | Implemented by KPC handymen Monitored by Parish Clerk & H&OS Committee Quarterly inspection carried out by an RPII Inspector (Wicksteed Leisure) on Inspector (Wicksteed Leisure) on 02/04/2019,29/10/2019 & 22/01/2020 |
| Wooden Aerial Runway | Children’s play area | Children General Public KPC Staff | med | Monitor wooden structures for natural cracking. Fill if larger than 10mm wide. Monitor damping spring and main cable Monthly operational inspection Yearly independent play inspection | Implemented by KPC handymen Monitored by Parish Clerk & H&OS Committee Quarterly inspection carried out by an RPII Inspector (Wicksteed Leisure) on Inspector (Wicksteed Leisure) on 02/04/2019,29/10/2019 & 22/01/2020 |
| Litter / Dog waste | Children’s play area | Children General Public KPC Staff | med | Play area fenced from dogs and no dogs signage on entrances. Weekly visual check | Weekly checks completed by KPC handymen. New dog control & dog waste signs installed March 2016. Signage reviewed by H&OS May & Oct 2019 |
| Vandalism | Children’s play area | Children General Public KPC Staff | Low | Weekly visual check Closure of any damaged equipment until assessed and repaired. | Implemented by KPC handymen Monitored by Parish Clerk & H&OS Committee. |